## Slide 1: Exam 3
AERO 4720 Aircraft Design II

## Slide 2: Problem 1: Subsonic Inlet Design [40 points]
Design flight condition:
  Freestream: density 0.3795 kg/m3, Mach 0.85, airspeed 252 m/s
  At inlet front face: Mach 0.63
  At engine front face: Mach 0.40
  Mass flow rate through engine: 540 kg/s
Find the inlet mass flow area () (in sq m) [10 points]
Find the inlet diameter (in meters) [15 points]
Find the engine front face diameter (in meters) [15 points]
Hints:
  Far upstream of the engine, use the continuity equation
  Use Eq. 10.16 and 10.17 to relate areas and
  Use Eq. 10.16 and 10.17 one more time to relate area to engine front face area

## Slide 3: Problem 2: Supersonic Pitot Inlet Design [40 points]
Design flight condition:
  Freestream: density 0.3795 kg/m3, Mach 1.40, airspeed 415 m/s
  At engine front face: Mach 0.50
  Mass flow rate through engine: 120 kg/s
Assuming a normal shock at the inlet, find the inlet Mach number (just downstream of the normal shock) [10 points]
Find the inlet diameter (in meters) [15 points]
Find the engine front face diameter (in meters) [15 points]
Hints: two of the three hints from Problem 1 apply here
From NACA Report 1135

## Slide 4: Problem 3 [20 points]
Solve this problem using the simplified “magic disk” thrust analysis model
Design flight condition:
  True airspeed: 212 m/s
  Air density: 0.46 kg/m3
  Thrust requirement: 20,000 N
Fill out the table for the four cases given below, where this design flight condition is achieved with four different magic disk areas. [Each case 5 points]
Case | Magic disk area [m2] | Mass flow rate [kg/s] | Accelerated flow speed, [m/s] | Propulsion efficiency (%)
1 | 0.4 |  |  | 
2 | 0.8 |  |  | 
3 | 1.2 |  |  | 
4 | 1.6 |  |  | 
Case | Magic disk area [m2] | Mass flow rate [kg/s] |  | Propulsion efficiency (%)
1 | 0.4 |  |  | 
2 | 0.8 |  |  | 
3 | 1.2 |  |  | 
4 | 1.6 |  |  |